Six Types of Simple Machines:

1) Levers					4) Inclined Plane

2) Pulleys					5) Screw

3) Wheel and Axle			6) Wedge

- Levers

( A bar that is free to pivot or turn, about a fixed point:

Fulcrum ( fixed point of a lever.

Effort Arm ( the part of a lever on which the effort force is applied.

Resistance Arm ( the part of a lever that exerts the resistance force.

Ex:

Using a crowbar to pry a lid from a box.

- Fulcrum ( the edge of the crate.

- Effort Arm ( the part that you push down on.

- Resistance Arm ( the part that exerts force on the lid.

Now, when we talk about Mechanical Advantage for a lever, we deal with the lengths of the arms of a lever (same as force in this case).

The length of the Effort Arm ( the distance from the fulcrum to the point where the force is applied.

Ex:

From the edge of the crate to where your hands are on the crowbar.

The length of the Resistance Arm ( the distance from the fulcrum to where the crowbar is putting force on the crate’s lid

Ex:

From the fulcrum to where the crowbar is putting force on the crate’s lid.

Formula for Mechanical Advantage:

MA=Le/Lr

# Le = length of the effort arm

Lr = length of the resistance arm

3 Types of Levers:

(

# Text boxes

Effort Arm is always shorter than the Resistance Arm