# Meters

- Galvanometer – an instrument used to determine current

- Made of a coil of wire connected to a circuit and suspended so it can rotate in the magnetic field of a permanent magnet

# How it works

- As current flows through the coil, magnetic force causes the coil to rotate against a spring.  A needle attached to the coil turns with it to provide a reading on a scale

# Two Types

- Ammeter ( measures current

- Voltmeter ( measures potential difference (voltage)

Electric Motors

- a devise that turns electrical energy into mechanical energy

  - contain an electromagnet that is free to rotate between 2 opposite poles of a permanent, fixed magnet

  - when current flows through the movable electromagnet, a magnetic field is produced

  - This causes enough attraction & repulsion with the permanent magnet to force the coil to turn

Generators

- Michael Faraday and Joseph Henry found that moving a wire though a magnetic field induced an electric current in a wire

( Process became known as electromagnetic induction

- Moving a magnet in and out of a coil of wire also produces a current

Generator ( Produces electric current by rotating a loop of wire in a magnetic field wire loop is connected to a source of mechanical energy and placed between the poles of a magnet

(  therefore it works opposite of an electric motor and

thus produces electrical energy from mechanical energy

## Direct and Alternating Currents

- Direct Current (DC) flows only in on direction through a wire

- - E- always move out of the (-) terminal toward the (+) terminal

Ex:

### Batteries

Alternating Current (AC) – reverses it direction in a regular pattern

Ex:

When you plug something into the wall outlet