Transformers

- a device that increases or decreases voltage of AC

- operates on the basis that voltage in one coil induces current in another coil

# Set Up

2 coils of wire wrapped around same iron core

- 1 coil is called primary coil

- 2 coil is called secondary coil

## Diagram of a Transformer

- current passes through primary coil causing it to create a magnetic field.  The magnetic field causes electromagnetic induction to occur which causes the 2nd coil of wire to have a current flow.

- if # of coils in primary equal # of coils in secondary, the voltage of coils will be equal

- if # of coils in primary are greater than # of coils in secondary the voltage of primary is greater than secondary

(called step-down transformer)

- if # of coils in secondary is greater than # of coils in primary, the voltage of secondary is greater than primary

(called step-up transformer)

-As electricity travels over long distances there is a loss of energy.  Power companies battle this by transmitting electricity of high voltages and low currents.  Less energy is wasted.

VOLTAGE	= 	SECONDARY

### RATIO			  PRIMARY

# Vs	=	Ns

## Vp		Np

Vp Ip	 =   Vs Is

because    Pp  =   Ps

Actual Pictures of Transformers

Typical transformer found outside your home.

Electrical substation with large transformers.