- Simple machine consisting of 2 wheels of different sizes that rotate together

Ex:

Doorknob

##### Faucet handle

- Effort force is usually applied to larger wheel.  The smaller wheel, called the axel, exerts the register force.

- Sometimes it is easier to think of a wheel and axel as being a lever attached to a shaft.

- The radius of the wheel is the effort arm and the radius of the axel is the resistance arm.  The center of the axel is the fulcrum.

###### Formula

MA = Radius of the wheel

## Radius of axel

rw

ra

Gears are like modified wheel and axel machines.  Effort is exerted on one of the gears causing the other gears to turn.

#### The larger gear ( effort gear

- The smaller gear ( resistance gear